## Slide 1: What are signals and systems
Examples of signals:
  Voltage output of a RLC circuit, stock market, ECG, speech, sequences of bases in a gene, MRI or CT scan
Examples of systems:
  RLC circuit, an algorithm for predicting future of stock market, an algorithm for detecting abnormal heart rhythms, speech understanding systems, edge detection algorithm for medical images.
Continuous vs. Discrete
x(t) x[n], n = …-2, -1, 0, 1, 2…

## Slide 2: Transformation of signals
Signal: x(t)
Scaling: a*x(t)
Time shift: x(t-t0)
Time reversal: x(-t)
Linear stretch: x(at) , a<1
Linear compression: x(bt), b<1
Examples: 0.5x(t), x(t-3), x(-t), x(t/2), x(2t), x(3-t/2)
-1 0 1
4
x(t)

## Slide 3: Periodicity
Continuous:
  x(t) = x(t+kT), k = 1, 2, … T: fundamental period
  Any sinuoid is periodic
  Ex: sin(2t/T)
Discrete:
  x[n] = x[n+kN], N: fundamental period
  Not all sinusoid is periodic!
  Periodic if 0/2 = m/N, where m and N are both integers (pg. 26 O & W)
  0/2 must be rational number
  Ex: sin( n), cos(4n/3), cos(2n)

## Slide 4: Special signals:
Sinc:
Delta function:
Unit step (CT):
Unit sample:
Unit step (DT):
Note: [t] = d/dt u[t] and d[n] = u[n] – u[n-1]